Topic	Type	Description
/world/world_demo/dynamic_pose/info	Pose	Full state (pose & twist) of all dynamic entities
/world/world_demo/model/tugbot/joint_state	JointState	All joint positions, velocities & efforts
Camera Back (RGB)
/world/.../link/camera_back/sensor/color/camera_info	CameraInfo (RGB)	Intrinsics & distortion parameters
/world/.../link/camera_back/sensor/color/image	Image (RGB)	Raw color frames
Camera Back (Depth)
/world/.../link/camera_back/sensor/depth/camera_info	CameraInfo (Depth)	Intrinsics for depth sensor
/world/.../link/camera_back/sensor/depth/depth_image	Image (Depth)	Depth image (per‐pixel distance)
/world/.../link/camera_back/sensor/depth/depth_image/points	PointCloud	Unprojected 3D point cloud
Camera Front (RGB)
/world/.../link/camera_front/sensor/color/camera_info	CameraInfo (RGB)	Intrinsics & distortion parameters
/world/.../link/camera_front/sensor/color/image	Image (RGB)	Raw color frames
Camera Front (Depth)
/world/.../link/camera_front/sensor/depth/camera_info	CameraInfo (Depth)	Intrinsics for depth sensor
/world/.../link/camera_front/sensor/depth/depth_image	Image (Depth)	Depth image (per‐pixel distance)
/world/.../link/camera_front/sensor/depth/depth_image/points	PointCloud	Unprojected 3D point cloud
Gripper Contact
/world/.../link/gripper/sensor/sensor_contact/scan	ContactScan	Distance readings around gripper
/world/.../link/gripper/sensor/sensor_contact/scan/points	PointCloud	Points where contact sensor “hits”
IMU
/world/.../link/imu_link/sensor/imu/imu	IMU	Accelerometer + gyroscope
Lidar
/world/.../link/scan_front/sensor/scan_front/scan	LaserScan (front)	2D range scan
/world/.../link/scan_front/sensor/scan_front/scan/points	PointCloud (front)	3D points from front lidar
/world/.../link/scan_back/sensor/scan_back/scan	LaserScan (rear)	2D range scan
/world/.../link/scan_back/sensor/scan_back/scan/points	PointCloud (rear)	3D points from rear lidar
/world/.../link/scan_omni/sensor/scan_omni/scan	LaserScan (omni)	360° 2D range scan
/world/.../link/scan_omni/sensor/scan_omni/scan/points	PointCloud (omni)	3D points from omni‐directional lidar

- Launch simulation (Gazebo or Isaac)
- Manually drive robot using keyboard or joystick
- Record data using a Python script or ROS2 bag
- Extract frames + commands, resize, and store

## Architecture Overview I
### 🔹 Input:
- image_seq: (Batch, Time, 1, 64, 64)
- lidar_seq: (Batch, Time, 64) → 64-beam LiDAR data
### 🔹 Model Flow:
1. CNN processes each frame → image_features
2. FC network processes each LiDAR scan → lidar_features
3. Both are concatenated into fused_features[t]
4. Fused features are passed through LTC neurons using odeint over time
5. Final hidden state is used to predict [linear_x, angular_z]
## Architecture Overview II
Input: (Batch, Time, 1, 64, 64) → 10 grayscale frames
CNN: Extracts spatial features from each frame
LNN: Evolves features over time using LTC neurons
Output: (Batch, 2) → [linear_x, angular_z]

Input sequence (video clip)
────────────────────────────────────────────────────────────────────────────
Shape: (B, T, 66, 200, 3)

        │
        ▼
[TimeDistributed CNN encoder] ← same CNN applied to EACH frame independently
────────────────────────────────────────────────────────────────────────────
For every t = 1..T:
  (66,200,3) ─Conv5x5,s2→ (31,98,24)
        Conv5x5,s2→ (14,47,36)
        Conv5x5,s2→ ( 5,22,48)
        Conv3x3,s1→ ( 3,20,64)
        Conv3x3,s1→ ( 1,18,64)
        Flatten → (1152)
        Dense100 → (100)
        Dense50 → ( 50)
        Dense128 → (128) = per-frame feature x_t

Stack features over time:
Output shape after TimeDistributed CNN: (B, T, 128)

        │
        ▼
[Liquid core: CfC (ncps)] ← the "liquid neurons" live here
────────────────────────────────────────────────────────────────────────────
RNN over time:
  h_t = CfC(x_t, h_{t-1}) (continuous-time dynamics with learnable time constants)

Input shape : (B, T, 128)
Output shape: (B, T, H) where H = hidden_dim (e.g., 128 liquid neurons)

        │
        ▼
[TimeDistributed Steering Head]
────────────────────────────────────────────────────────────────────────────
For every t:
  h_t → Dense64(ReLU) → Dense1(linear) → ŷ_t (predicted steering at time t)

Output shape: (B, T, 1)
load a batch → CNN encode → CfC → output → backprop → next batch.
Quick decision tree
Train 1×CfC(128).
  - Underfits? → try 1×CfC(192) or (256).
  - Still underfits? → 2×CfC (128→64) with dropout 0.15 and clipnorm.
  - Overfits? → reduce hidden_dim or increase regularization/augmentation.

Imu senosr topic
entity_name: "tugbot::imu_link::imu"
orientation {
  x: 4.7667540498731861e-07
  y: 3.5466561305861331e-07
  z: 0.59846353674410624
  w: 0.80115004536440171
}
angular_velocity { rad/s
  x: 4.7045270970681156e-14
  y: -5.2406113955569839e-14
  z: 3.0809133840712358e-15
}
linear_acceleration { m/s2
  x: 2.2191654280798264e-08
  y: 1.164519685164992e-05
  z: 9.8000000000008214 gravity
}

header {
  stamp {
    sec: 1182
    nsec: 990000000
  }
  data {
    key: "frame_id"
    value: "tugbot::imu_link::imu"
  }
  data {
    key: "seq"
    value: "2957"
  }
}

bridge the topic
ros2 run ros_gz_bridge parameter_bridge \
  /world/world_demo/model/tugbot/link/camera_front/sensor/color/image@sensor_msgs/msg/Image@gz.msgs.Image \
  /world/world_demo/model/tugbot/link/scan_front/sensor/scan_front/scan@sensor_msgs/msg/LaserScan@gz.msgs.LaserScan \
  /model/tugbot/odometry@nav_msgs/msg/Odometry@gz.msgs.Odometry \
  /model/tugbot/cmd_vel@geometry_msgs/msg/Twist@gz.msgs.Twist
inside the workspace
1. chmod +x src/tugbot_recorder/tugbot_recorder/recorder.py
2. colcon build
3. source install/setup.bash
  do this in every new terminal before running your package
4. ros2 run tugbot_recorder recorder

Using Ros2 bag is option to record all the topic values and then convert or down sample the data to required format

LNN without nav2
For each timestep t, feed:
1. Camera image → perceives the environment (aisles, racks, people).
2. Current visible marker(s) → IDs and relative poses (distance & angle).
3. Optional odometry → velocity, angular velocity (helps with smooth motion).
So input could look like:
[ image_t , visible_marker_IDs_t , relative_poses_t , odometry_t ]

LNN with nave2